Tach rev 2 errata

Caps next to charge pump supply are 0402, should be 0805.
X27.589 footprint missing two mounting posts
Voltage measurement +12V for ADC missing
jtag needs to have NRST on pin 9
Should probably set up the current source on +5V or even +12V. Then divide down the output, maybe bias above GND. Would allow measurement of lower temperatures.
TIM3 CH2 / pin A7 has NO DMA TRIGGER. Must use pin A6.